## Slide 1
CONFIDENTIAL WORKING DRAFT, v0.7 . NOT FOR DISTRIBUTION
Katla Readiness Assessment
Chapter 4: Volcanic gas geochemistry and monitoring capability
Prepared for institute management
Author: Martha Glass, Natural Hazards Division
Contributing: Dr. Helgi Bjornsson, glaciology and jokulhlaup scenarios
Submission target: 2 October 2026

## Slide 2
What this chapter does
It states what gas geochemistry can currently measure at Katla, where the gaps are, and what must be in place so a change in degassing is recognised early and communicated cleanly to civil protection.
The complication
Katla sits beneath an ice cap, which limits direct gas sensing and couples any escalation to rapid melt and flooding.
The objective
Narrow and practical: recognise a real change, and avoid both false alarms and missed onset.
Katla Readiness Assessment . Chapter 4 . Confidential working draft

## Slide 3
Current monitoring capability
Remote scanning
Sulphur dioxide flux in any plume that clears the ice.
Direct sampling
Species ratios when the caldera rim is accessible.
Drone sensing
Reach over terrain that is unsafe to approach on foot.
All three methods are constrained by the ice cap and by weather windows. None alone is sufficient, and the chapter treats them as one combined capability.
Katla Readiness Assessment . Chapter 4 . Confidential working draft

## Slide 4
Capability matrix
Method | Detects | Main limitation | Readiness
Plume scanning | SO2 flux | Needs a plume clear of ice | Operational
Direct sampling | Gas ratios | Rim access and weather | Partial
Drone payload | Local gas in plume | Battery and wind limits | Operational
Caldera baseline | Reference values | Updated data missing | Gap
Katla Readiness Assessment . Chapter 4 . Confidential working draft

## Slide 5
KNOWN GAP
Updated baseline gas measurements from the caldera rim are missing.
Without a current baseline, a real change is harder to recognise quickly. The July 2025 highland campaign began this work at the rim, and a further visit is needed before the assessment is final.
Katla Readiness Assessment . Chapter 4 . Confidential working draft

## Slide 6
Recommendations
1
Close the caldera rim baseline gap in the next accessible field window.
2
Keep gas, deformation, and seismicity read together, never in isolation.
3
Hold the agreed communication path to civil protection, observation before forecast.
4
Finalise the chapter for submission on 2 October 2026.
Martha Glass . Natural Hazards Division . Confidential working draft