## Slide 1
⚠ MANDATORY CREW SAFETY TRAINING ⚠
Concrete Pour Operations & Fall Protection
Harrison 24-Unit Residential Build · 330 Bergen Ave, Harrison, NJ
Conducted by: Lisa Reyes, Foreman · Laborers' Local 472 · OSHA 30-Hour Certified
Training Date: November 20, 2026 · Pre-Pour Mandatory Sign-Off Required
29 CFR 1926.502, Fall Protection 29 CFR 1926.702, Concrete & Masonry Construction

## Slide 2
Why It Matters
#1
Cause of Fatal Construction Injuries
FALLS
#2
OSHA Citation Category 2025
FALL PROTECTION
36%
of Construction Deaths involve Concrete Work
NATIONWIDE
$14K+
Average OSHA Fine per Serious Violation
PER INCIDENT
Every person on this site goes home at the end of the day. That is not negotiable.
Fall protection required at ANY elevation above 6 feet, no exceptions, no shortcuts.
Concrete work kills when formwork fails, workers are not properly anchored, or PPE is skipped.
This crew has zero lost-time injuries in 2026. We keep it that way through December.
Violations will be documented and reported immediately to Tony Rizzi and Frank Delmonico.

## Slide 3
Required PPE, Concrete Pour Day
HARD HAT
ANSI Z89.1 Class E Required at all times on site
HIGH-VIS VEST
ANSI/ISEA 107 Class 2 Required during pour and delivery
STEEL-TOE BOOTS
ASTM F2413 rated No exceptions, concrete is 4,000+ PSI
HEARING PROTECTION
NRR 25+ recommended Mandatory during pump operation
GLOVES
Chemical-resistant gloves Wet concrete causes alkaline burns
EYE PROTECTION
Safety glasses or goggles Required during pour and finish
FALL HARNESS
Full-body harness + lanyard Mandatory above 6 ft elevation
RESPIRATORY
N95 or better For dry mix handling and grinder work
Failure to wear required PPE = immediate stop-work order. No warnings on pour day.

## Slide 4
Pre-Pour Safety Checklist (Dec 9, 2026 · 5:00 AM Start)
FORMWORK
☐ Formwork inspected by Hector Vega the day prior
☐ All bracing and shoring verified per engineering specs
☐ No deformation, bowing, or gap > 1/16 in.
☐ Runoff/bleed water drainage paths confirmed clear
EQUIPMENT
☐ Concrete pump truck positioned and chocked
☐ Boom radius verified, no overhead utility conflict
☐ Vibrators tested and backup unit on site
☐ Chutes and hoppers clear of debris
SITE SAFETY
☐ Perimeter barriers and warning tape in place
☐ Fall protection anchors verified for elevated pours
☐ First-aid kit and eyewash station staged at trailer
☐ Emergency contact list posted: L. Reyes 973-XXX-XXXX / Tony Rizzi 973-555-0412
WEATHER & LOGISTICS
☐ Temperature forecast: above 40°F, proceed; 32 to 40°F, heat blankets staged
☐ Wind speed below 25 mph, proceed; above, hold and reassess
☐ Ready-mix truck schedule confirmed (3 trucks, 30-min intervals)
☐ Cure time minimum 24 hours before any load application
All checklist items must be initialled by Lisa Reyes before first truck arrives.

## Slide 5
Emergency Response Protocol
STOP
Immediately halt all work. Yell 'STOP WORK', everyone within earshot repeats it.
CALL
Dial 911 first. Then call Lisa Reyes (site foreman). Do not move an injured worker.
SECURE
Establish a 20-ft exclusion zone around the incident. Designate a spotter.
ASSIST
Trained first-aiders administer aid until EMS arrives. First-aid kit at the trailer.
DOCUMENT
Foreman documents incident start time, witnesses, photos. Report to Tony Rizzi within 1 hour.
REPORT
OSHA 300 log entry within 24 hours. Serious injury: OSHA verbal report within 8 hours.
Key Numbers: 911 · Lisa Reyes · Tony Rizzi 973-555-0412 · Hector Vega 908-555-0378

## Slide 6
Crew Acknowledgement & Sign-Off
By signing below, I confirm I have received, understood, and will comply with this safety training.
Worker Name (Print) | Badge / ID | Signature | Date
Training Conducted By: Lisa Reyes, Foreman
Date: _________________ Signature: _____________________
Superintendent Review: Tony Rizzi
Date: _________________ Signature: _____________________