## Slide 1
Water Quality and Biosecurity
Recirculating system operating standards and daily controls
Bayshore Sustainable Aquaculture | Grow-out Hall A | Anthony Cross and Jake Dawson

## Slide 2
Daily Control Targets
Parameter | Target band | Action point | Read at
Temperature C | 28 to 30 | above 31 | 05:00 and 14:00
Dissolved oxygen mg/L | 6.0 to 7.5 | below 5.0 | 05:00
pH | 7.6 to 8.2 | below 7.4 | 05:00
Salinity ppt | 17 to 21 | outside band | 05:00
Ammonia TAN mg/L | under 0.4 | above 0.5 | 05:00
Nitrite NO2 mg/L | under 0.5 | above 0.6 | 05:00
Readings logged at five each morning with the multiparameter meter. Action points trigger a same-day check, not a wait-and-see.

## Slide 3
January 2026 Temperature Trend
Chart: 
| Jan 1 | Jan 8 | Jan 15 | Jan 22 | Jan 29
Dawn temp C | 28.6 | 29.4 | 29 | 28.9 | 29.2
Afternoon temp C | 29.7 | 30.1 | 30 | 29.8 | 30.2
- Dawn to afternoon swing held near one degree
- No action points hit in the month
- Band stayed inside 28 to 30 at dawn
- Stable water means steady molt and growth

## Slide 4
Biosecurity Routine
Every day
- Foot bath at the door
- Tray check and feed response
- Mortality count and removal
- Meter round at five
Every week
- Filter and biofilter check
- Salinity and alkalinity dose
- Net and tool disinfection
- Backup pump test

## Slide 5
Ammonia and Nitrite Watch
Chart: 
| Jan 1 | Jan 8 | Jan 15 | Jan 22 | Jan 29
Ammonia TAN mg/L | 0.3 | 0.23 | 0.27 | 0.22 | 0.26
Nitrite NO2 mg/L | 0.41 | 0.24 | 0.49 | 0.37 | 0.22
- Ammonia held under the 0.4 action point all month
- Nitrite stayed under 0.5 with one near touch
- Biofilter carrying the load as planned
- Water changes timed to the dawn round

## Slide 6
Clean water is the whole job. Everything else follows it.
Disease consult on call with Dr. Sarah Hutchins at the Lonestar Foundation extension for any outbreak.
Bayshore Sustainable Aquaculture | anthony.cross@Greenridertech.co