## Slide 1
GARAGE WORKSHOP
Toy Chest Build Walkthrough
A solid poplar toy chest with a soft-close lid. Built for Sophie, and meant to outlast her.
For Sophie, age 5
Detached garage workshop, 118 Sedgwick Street
Started October 2026

## Slide 2
WHAT WE ARE BUILDING
The goal
Workshop notes | 118 Sedgwick Street | Build for Sophie
2
| Solid and square. Nothing fancy, but something she will still have when she is grown.
| A soft-close lid so it settles slow and never catches a small finger. That is the whole reason for the design.
| Three-quarter-inch poplar for the body. Paints clean and takes a knock.
| Half-inch birch plywood bottom, floating in a groove so it cannot rack or rattle.
| Corner posts to tie the panels together and give it strength where a kid will sit and stand on it.

## Slide 3
MILL TO THESE SIZES
Cut list
Workshop notes | 118 Sedgwick Street | Build for Sophie
3
Part | Qty | Material | Thickness | Size (in)
Front / back panel | 2 | Poplar | 3/4 in | 30 x 16
Side panel | 2 | Poplar | 3/4 in | 15-1/2 x 16
Bottom | 1 | Birch plywood | 1/2 in | 29 x 15
Lid glue-up | 1 | Poplar | 3/4 in | 31 x 17
Lid cleats | 2 | Poplar | 3/4 in | 15 x 2
Corner posts | 4 | Poplar | 1-1/2 in | 1-1/2 x 18
Base trim | 4 | Poplar | 3/4 in | 3 wide, cut to fit
Groove for the bottom is 1/4 in wide by 3/8 in deep, set 1/2 in up from the bottom edge of every panel. Cut it before assembly.

## Slide 4
DO IT IN THIS ORDER
Order of work
Workshop notes | 118 Sedgwick Street | Build for Sophie
4
1. Mill all parts to the cut list. Label each piece in pencil.
2. Cut the groove for the plywood bottom in every panel before assembly.
3. Dry fit the whole box and check it for square, corner to corner, before any glue.
4. Glue and clamp the sides with the bottom floating in its groove. Leave it clamped overnight.
5. Glue up the lid, then flatten it and hold it flat with the cleats underneath.
6. Round every edge and corner with the router. No sharp corners anywhere a kid will touch.
7. Sand to 220, seal, then two coats of clear poly, sanding lightly between coats.
8. Hang the soft-close hinges and the safety lid stay last, after the finish is fully cured.

## Slide 5
THE PART THAT MATTERS MOST
Safety and finishing
Workshop notes | 118 Sedgwick Street | Build for Sophie
5
220
Final sanding grit
2
Coats of clear poly
1
Safety lid stay, non-negotiable
| The safety lid stay is the whole point. It holds the lid open and lets it down slow. She is five.
| Let Sophie pick the knob. She likes the red ones. Her chest, her call.
| Burn her initials inside the lid so she knows Grandpa made it for her.
| Round every edge one more time by hand before the finish. Then check it with your palm.
| Keep the finish food-safe and fully cured before it goes in the house.