## Slide 1
AVALANCHE LEVEL 1
Reading the Snow, Reading the Slope
A two day field course in recognizing avalanche terrain, understanding the snowpack, and making safer decisions in a group.
Instructor Jeff Peterson, Avalanche Level 3
Provider Teton Summit Resort Avalanche Education
Meeting point Teton Pass winter lot, 7:30 AM

## Slide 2
01
Why this course exists
Most people caught in avalanches trigger the slide themselves. The goal of this weekend is to give you the judgment to avoid that, and the skills to rescue a partner if it happens.

## Slide 3
THE CASE FOR TRAINING
The problem in three numbers
90%
of avalanche fatalities are triggered by the victim or someone in the party
15 min
the window where a buried subject has the best chance of survival
3
tools every traveler carries, transceiver, probe, and shovel
Avalanche safety is a decision making skill first and a rescue skill second. We train both.

## Slide 4
MODULE ONE
How an avalanche forms
Slab
A cohesive layer of snow bonded over a weaker layer below.
Weak layer
Facets, surface hoar, or a buried crust that fails under load.
Trigger
Added weight, often a skier, that tips the balance.
Slope angle
Most slides release on slopes between 30 and 45 degrees.

## Slide 5
MODULE TWO
Terrain is the one thing you control
Higher consequence
• Slopes 30 to 45 degrees
• Convex rolls and wind loaded features
• Terrain traps, gullies and trees
• Connected slopes above you
Lower consequence
• Slopes under 30 degrees
• Supported, planar terrain
• Ridgelines and dense timber
• Open runouts with no trap

## Slide 6
MODULE THREE
The daily advisory is your starting point
Read it every morning
Hazard rating, problem type, aspect, and elevation.
Match it to your plan
Avoid the aspects and elevations called out as the problem.
Watch for red flags
Recent avalanches, shooting cracks, whumpfing, rapid warming.
Plan a margin
Pick terrain that still works if the forecast is one notch off.

## Slide 7
MODULE THREE
North American danger scale
Rating | Likelihood | Travel advice
Low | Unlikely | Generally safe, watch isolated features
Moderate | Possible on specific features | Evaluate snow and terrain carefully
Considerable | Likely on the problem feature | Conservative terrain choices
High | Very likely | Avoid avalanche terrain
Extreme | Certain and large | Stay out of avalanche terrain

## Slide 8
02
Companion rescue
If a partner is buried, you are the rescue. No outside help arrives in time. The next slides are the sequence we practice until it is automatic.

## Slide 9
MODULE FOUR
The rescue sequence
Watch and mark
Keep eyes on the subject, note the last seen point.
Switch to search
All transceivers to search, call the group, pick a leader.
Signal search
Move fast to first signal, then bracket the flux line.
Pinpoint and probe
Fine search in a grid, probe to confirm, then dig.
Strategic shoveling
Dig in from downhill, move snow, expose the airway first.

## Slide 10
MODULE FOUR
Why speed is everything
Chart: 
| 0 to 15 min | 15 to 30 min | 30 to 45 min | Over 45 min
Approx survival rate, percent | 92 | 30 | 24 | 14
Survival falls sharply after the first fifteen minutes. A practiced party is the difference.

## Slide 11
LOGISTICS
What to bring on course day
Required
• Transceiver, probe, shovel
• Touring setup or splitboard
• Full winter layers
• Food and water for a full day
Notes
• Rentals available on request
• No scented products, wildlife country
• Arrive for the trailhead beacon check
• Course runs in most weather

## Slide 12
LOGISTICS
Two day schedule at a glance
Day | Morning | Afternoon
Day one | Terrain and the advisory | Companion rescue and burial practice
Day two | Snowpack tests in a pit | A tour with real decisions

## Slide 13
Your takeaway for every tour
→ Plan the day against the advisory before you leave the trailhead.
→ Choose terrain with a margin, not terrain at the edge of the forecast.
→ Carry the gear, and practice the rescue until it is muscle memory.
→ The best decision in avalanche terrain is usually the humble one.
Jeff Peterson, Avalanche Level 3, Teton Summit Resort Avalanche Education