## Slide 1
WESTERN RESERVE WOODTURNERS GUILD
Intermediate Woodturning
End Grain, Sealing, and Hollowing
Second Saturday class | 10:00 AM to 12:00 PM
Instructor: Charles Ferguson

## Slide 2
This morning at the bench
1
Why end grain checks
10:00 to 10:20
2
Seal a blank, hands on
10:20 to 10:40
3
Mount, true, set the rim
10:40 to 11:15
4
Start the hollow, light cuts
11:15 to 11:50
5
Clean up, questions, practice
11:50 to 12:00

## Slide 3
Why end grain checks
Green wood loses moisture fastest through the end grain.
▪ Ends dry faster than the middle, so the wood splits as it shrinks unevenly.
▪ Seal both end grain faces the day you get the blank, not next week.
▪ Two coats, letting the first soak in before the second.
▪ Label species and date, then store off the concrete on a rack with airflow.
▪ A consistent habit beats the best sealer used once in a while.

## Slide 4
Tool setup for hollowing
Bowl gouge, half inch
Truing and shaping the outside
Bowl gouge, three eighths
Refining the rim and inside near the top
Hollowing tool
Reaching the lower inside wall
Calipers
Checking wall thickness as you go

## Slide 5
Safety, every time
Tool rest close
and just below center.
Face shield on
sleeves rolled, nothing loose near the lathe.
Stop the lathe
before you reach in to check anything.
If the wood fights you
reset the rest or resharpen, do not muscle it.
We learn more from a wall that blew out than from one that went perfectly.